## Slide 1: Bblr
Xavier de Gunten
David Spruill
Elder Yoshida

## Slide 2: Last Week
Troubleshooting
  Not enough airflow, bad solenoids, bad check valves

## Slide 3: Air supply
Pump Rated at 25Nl/min
  How fast can we switch all 24 without running out of air?
Rails | 24 | units
Raw Airflow | 25 | Lpm
Bubble Diameter | 1.4 | cm
Bubble Volume | 1.1494E-05 | m^3
Bubbles Frequency | 1.510444598 | Hz

## Slide 4: Airflow through orifice
Ta : Air Temperature (°C)
p1 : Primary Pressure (kPa abs)
p2 : Secondary Pressure (kPa abs)
do : Diameter of Orifice (mm)
C : Discharge Coefficient
Qa : Air Flow Rate (Normal) (Nm³/min)
Fγ : Specific heat ratio factor
xT : Pressure differential ratio factor (=0.72)

## Slide 5: Airflow through orifice
Diff. Pressure of 2psi, 0.17”ID tube => 31.08 Nl/min
  Need to account for tube length, T-Joint, etc...

## Slide 6: Ensuring proper air distribution
Properly sized tubing and divider (2x12)
  0.17”ID and 5/16”ID tubing
  5/16”ID => 444.128Nl/min of airflow

## Slide 7: New check valves…
Not very good
  Need high input pressure
  Makes noise when open
  Prone to leakages (bad seal)

## Slide 8: On the current display…
Tried to clean it up so that we could work on it in the lab with water (less messy)
  Frozen and broken hose…
Ordered 10 replacement solenoids