## Slide 1: Bblr
Xavier de Gunten
David Spruill
Elder Yoshida

## Slide 2: Trobleshooting
What went wrong?
  Clogged check valves?
  Circuit malfunction?
  Bad solenoids?
  Wrong combination of pressure, pulse width?
  Uneven distribution of air?

## Slide 3: Controlled Environment
Study different combinations of parameters
Setup
  Air tank – uninterrupted airflow
  Pressure gauge
    Calibrate initial tank pressure & pump cutoff pressure
    Read pressure with better precision

## Slide 4: Setup
Air Tank
Pressure Gauge
Pump

## Slide 5: Huh? Problems are gone!

## Slide 6: Results
Solenoid having trouble to hold pressure at 15psi
  Small Bubbles coming up
  ~ 6.5ms too low to be consistent
Very consistent results for pressures below 12psi
12V solenoid input, 1Hz pulse frequency, pulse width >7.8ms